## Slide 1: Software Lab Presentation - Group 25
Munich, 18 July 2025
TUM School of Engineering and Design
Speaker: Nien-Ying (03803153)

## Slide 2: Festo Plant for Discrete Manufacturing: Developing Simulation Models for Industrial Copilot
Presentation by MSc. Computational Mechanics students:
Adrián Almohalla (03804037)
Eduardo Silva (03805057)
Nien-Ying Lin (03803153)
Monitored and coordinated by:
Mohamed Khalil
Speaker: Nien-Ying (03803153)

## Slide 3
Overview
Quick Recap
Dataset Explained
Degradation Tool
Agentic System
Next Steps & Timeline
Speaker: Nien-Ying (03803153)

## Slide 4: Quick Recap About Team
Eduardo Silva
Mohamed Khalil
khalil.mohamed@siemens.com
Siemens Technology Center (Garching)
Adrián Almohalla
Nien-Ying Lin
Speaker: Nien-Ying (03803153)

## Slide 5: Quick Recap About Problem
Problem:
Manufacturing involves process (feed rate, torque) and product (material) parameters
Existing simulation tools are complex and not accessible to non-experts.
Fig.1 - Festo Plant Drilling Station
Speaker: Nien-Ying (03803153)
Fig. 2 - RAG-LLMs Tools
Notes: Explain here what the problem is.
Use the documents from Siemens that they gave us for the software lab to explain what the problem is.

## Slide 6: Example User Case
“What is the expected energy consumption for a drilling process using an 14 mm drill bit on a copper plate? And how does it change with time?
“How much wear can I expect this production order to cause to my drilling tools?
“If I use X material, how does it change the quality of my drilling? And how can I optimize it?”
Fig. 3 - User Case Icons
Speaker: Nien-Ying (03803153)

## Slide 7: Dataset Overview
Speaker: Nien-Ying (03803153)
Feature | Unit | Description
ID | — | Unique identifier for each row
vc (Cutting speed) | m/min | Generated: Walter GPS
n (Spindle speed) | 1/min | Calculated: (vc × 1000)/(π × D)
f (Feed) | mm/rev | Generated: Walter GPS
vf (Feed rate) | mm/min | Calculated: f × n
Pc (Power) | kW | Calculated: (F × vc)/1000
Cooling | % | Assigned: 0, 25, 50, 100
Material | — | Assigned: P(C45K), K(GJL-250), N(AlSi alloy)
Drill Bit type | — | Assigned(DIN 1836): N(for C45K), H(for GJL-250), W(for AlSi alloy)
t (Process Time) | sec | Generated: Walter GPS
Failure Labels | Unit | Description
Main Failure | binary | Rule-based: 1 if any subgroup failure occurs
Build-up Edge | binary | Rule-based: Low vc + low cooling
Compression Chips | binary | Rule-based: ≥2 of: high vf, low cooling, wrong bit
Flank Wear | binary | Rule-based: High vf + low vc
Wrong Drill Bit | binary | Rule-based: Bit–Material mismatch
20,000 synthetic drilling operations
Each row contains:
  10 features, 5 failure labels
  Fixed drilling target: blind hole (⌀12 mm, depth 60 mm)
D: drill bit diameter, F: drilling force
[1]

## Slide 8: Torque vs. Feed
Speaker: Nien-Ying (03803153)
Fig. 4 - Torque vs. Feed across materials and cooling levels, colored by failure status.
To observe how torque varies with feed, and whether this relationship is influenced by:
Material type (N, P, K)
Cooling level (0, 25, 50, 75, 100%)
Main failure occurrence (True / False)
Cooling
Torque [Nm]
Feed [mm/rev]
Material

## Slide 9: Torque vs. Feed & Cutting Speed
Speaker: Nien-Ying (03803153)
To observe torque is affected by:
Feed (left)
Cutting speed (right)
under different materials (N, P, K).
Conclusions
Torque increases linearly with feed.
Cutting speed also influences torque, but much less than feed.
Fig. 5 - Torque vs. Feed and Cutting Speed, colored by Material

## Slide 10: Torque Regression
Speaker: Nien-Ying (03803153)
Model: Linear Regression (Implemented in Python using Scikit-learn)
Features:
  Feed f [mm/rev]
  One material property ( Hardness [Brinell], Young's Modulus [GPa], Poisson’s Ratio )
Target (Label):
  Torque (calculated from power and spindle speed)
Features | R² Score | Coefficients (Feed / Property) | Comment
Feed, Hardness | 0.8925 | +2338.64 / −9.98 | Stable model with good accuracy
Feed, Young’s Modulus | 0.6813 | −756.90 / −9.73 | Low R²
Feed, Poisson’s Ratio | 0.9935 | +8570.38 / +15984.66 | High R² but very large coefficients
Torque [Nm] = 2727.15 + 2338.64 × Feed f [mm/rev] + -9.98 × Hardness [Brinell]
Notes: higher hardness gives lower torque, because in this dataset, harder materials like cast iron are easier to cut, while softer and more ductile materials like aluminum alloys create more cutting resistance.

## Slide 11: Degradation Tool
Speaker: Adrián (03804037)
[1]

## Slide 12: Degradation Tool
Speaker: Adrián (03804037)
New form of estimating wear:
Look for best correlation between material and, properties and Failure.
FWF =1 => 100% wear
Fig. 6 - Degradation Tool Options

## Slide 13: Degradation Tool
Speaker: Adrián (03804037)
For each material:
- A Linear Regression model for Torque prediction.
- An XGBoost Classifier for predicting wear zones (3 classes). We use SMOTE to balance class distribution.
Training models quality and example for an input:
Fig. 7 - Failure Criteria

## Slide 14: Future Tools and Improvements with Degradation
Speaker: Adrián (03804037)
Degradation model
Energy consumption model
Provided model by Siemens
Connect it with the LLM

## Slide 15: LangGraph Agent System - ChatBot
Creating a simple ChatBot model.
Usage of open-source & free models collection Ollama. [2]
Skeleton of structure to build on top of.
Speaker: Eduardo (03805057)
Fig. 8 - ChatBot Case

## Slide 16: LangGraph Agent System - Dummy Tool
Creation of a dummy tool to test implementation.
Inputs and functionality comments needed.
Return as explanation highly improves results!
After tools are developed, easy implementation due to compartmentalization.
Speaker: Eduardo (03805057)
Fig. 9 - Dummy Tool

## Slide 17: LangGraph Agent System - Architecture
First step, create a single agent system.
Agent responsible for usage of dummy tools.
Test tool calling by different models. [3]
Test output by different models.
Speaker: Eduardo (03805057)
Fig. 10 - Single Agent

## Slide 18: LangGraph Agent System - Results
Model calls the correct tool!
The output from the tool is usually always right since it is basic python tool calling.
ReAct model correctly explains the formula.
Speaker: Eduardo (03805057)

## Slide 19: LangGraph Agent System - Results
Speaker: Eduardo (03805057)
Possible to check reasoning process of model.
Capture reasoning errors early.
Very important for next step of development.

## Slide 20: Next Steps
Implement tools for degradation and failure of drilling bit.
Evaluate how to predict quality of drilling based on these aspects.
Expand single-agent calls to multi-agents systems or more complex architectures.
Evaluate Prompt Engineering and Features Importance.
Speaker: Eduardo (03805057)
Fig. 11 - Multi-Agent System

## Slide 21: Timeline
01/09/2025
Start of Refinement Stage
Evaluate different models and optimization.
01/12/2025
Final Presentation
Present final results
01/07/2025
Second Presentation
Have 1 or 2 tools implemented with LangGraph System
Speaker: Eduardo (03805057)
“You are here”
Finalize degradation and energy tools.

## Slide 22: Documentation and Literature
Refer to our Github to get all the code, reports and documentation!
QR code leads to our Github repository.
Speaker: Eduardo (03805057)

## Slide 23: References
[1] - Explainable Artificial Intelligence in Mechanical Engineering: A Synthetic Dataset for Comprehensive Failure Mode Analysis http://dx.doi.org/10.1109/TransAI60598.2023.00032
[2] - Ollama Models Collection, https://github.com/ollama/ollama
[3] - Tool Calling LangGraph, https://langchain-ai.github.io/langgraph/how-tos/tool-calling/#toolnode
References from other presentation already in GitHub!
Speaker: Eduardo (03805057)